## Slide 1: Global sensitivity analysis methods for Monte Carlo radiation transport solvers
Preliminary Research Proposal
Kayla Clements
Advisor: Dr. Todd Palmer
School of Nuclear Science and Engineering
February 6, 2023
Notes: Reminders from TP:
As you think about your slides, I recommend illustrating concepts with simple examples, if possible, and skipping details of derivations.
Being able to convince your committee that what you plan to do is a) new, and b) needed is an important part of the proposal/presentation. I typically want to see some evidence when I am being persuaded, and that’s where familiarity with previous research is important.

## Slide 2: Background – Computational modeling
Computational modeling diagram[1].
Data
Model
Simulation
Test simulation
?

## Slide 3: Background – Uncertainty quantification (UQ)
Forward uncertainty propagation in computational models[2].
Uncertainty propagation and analysis
Assume accurate model (i.e. no more model parameter tuning).
Uncertainty in system parameters, source terms, systems conditions (initial/boundary).
Propagate uncertainty through model by performing simulations.
Necessary for predictive simulation, robust design, and failure analysis.
Characterize response as function of uncertain parameter(s).

## Slide 4: Context – Global sensitivity analysis (GSA)
Multiple sources of uncertainty
Quantify uncertainty caused by each uncertain parameter.
Understand parameter interactions.
Improve model robustness and reliability.
Prioritize uncertainty reduction.
Uncertainty propagation
Uncertainty analysis
Global sensitivity analysis

## Slide 5: Motivation – Stochastic solvers
Forward uncertainty propagation with stochastic computational model[2].
Uncertainty propagation and analysis
Stochastic models have inherent uncertainty.
Propagate uncertainty through model by performing simulations.
Characterize response as function of uncertain parameter(s), but computational model has introduced additional uncertainty.
Stochastic Model
Stochasticity
Global sensitivity analysis
Complicates parameter propagation and interactions complicates GSA

## Slide 6: Context – Monte Carlo radiation transport (MCRT)
Monte Carlo Radiation Transport
Initialize particle
Sample distance to next collision
Stream particle – boundary? collision?
Continue until particle is has interaction or exits system
Start again with a new particle until all particles have finished
Repeat for all histories, recording tallies for quantities of interest
x=0
x=L
Streaming Particle
Quantities of interest
Notes: - speaking of monte carlo, pivot to MC rad transport
- this is a very simple rad transport system with some particles streaming
As palmer said, deterministic solve continuous across entire phase space
MC treats physical system as statistical process
- nuclear data for probability distributions
- look at transport algorithm as sampling approach, sampling distributions to tally particle behavior, avg QoI
- variance function of method
- introduce some stochasticity *click*
- want to perform UQ to understand effect, sampling approach
*click*
- however, we know any variance at the end is a result of the solver AND the parameter
- novelty of method is ability to deconvolve w/ tallies that already exist
Pivoting a little bit here, we’ll look at some background for Monte Carlo radiation transport that is I’m sure redundant for many of you. Monte Carlo transport can be used to solve for a QoI as an alternate to deterministic methods, which would explicitly solve a system like this and, for example, get a solution of flux across the entire phase space. Instead, MC methods treat the physical system as a statistical process, using nuclear data to construct probability distributions that describe the various ways particles could behave in the system. Individual particles are simulated and their behavior, like colliding with other particles, exiting the system, etc., is recorded in tallies based on what information the user might want. The central limit theorem can then be applied to extrapolate the tallied behavior of the simulated particles to the average behavior of all particles in the system, with some associated uncertainty based on the number of particles simulated.
This can also be thought of as a sampling approach – you run a certain number of histories and end up with a tally response for each, and you can calculate the mean and variance of your response. The variance you would see here would be a function of the method itself, where increasing the number of histories would decrease the variance.
What if we introduce some stochasticity to our monte carlo problem, for example some uncertainty in the total cross section? *click* We can perform UQ to understand the uncertainty of this parameter propagates throughout the solution by following a sampling UQ approach, which might look something like this *click* where we’ve nested the monte carlo transport solver into the monte carlo for UQ. Ideally, the UQ analysis that we perform for the variance would give the variance of our solution as a function of a UQ parameter. However, we know our QoI is already uncertain as a function of the solver itself; simply computing the variance of our realizations would give over-estimate the variance in a UQ sense, because the solver is adding additional stochasticity. The novelty of the method I’ll introduce now is that it’s able to deconvolve the parameter and solver uncertainties in the solution, and does so using information that a monte carlo transport solver would already tally.
You mentioned here that Monte Carlo is an algorithm rather than a set of equations. This is a bit contentious--some claim that Monte Carlo is nothing more than solving the equations in a different way. Personally, I think show how Monte Carlo solves the equations, but that, really, it's an algorithm for simulating phenomena. Nonetheless, if you make that statement, "them's fighin' words," such that I'd suggest not saying that so that you don't potentially pick a fight you don't want and distract your viewers.

## Slide 7: Research proposal
Goal: Quantify and mitigate the effects of performing UQ and GSA on stochastic computational models.
Research objectives:
  UQ – Develop robust theory for an accurate, efficient, and broadly applicable variance deconvolution estimator for uncertainty quantification with stochastic solvers.
  GSA – Understand how use of a stochastic solver affects both sampling-based and PCE surrogate- based GSA. Develop methodologies to use stochastic solvers in GSA by explicitly accounting for the variability they introduce.
  Transport – Demonstrate applicability of developed UQ and GSA methods by applying them to more complex and realistic radiation transport using CEMeNT’s MC/DC codebase. Understand how the cost of the approaches change with tally mesh resolution.
Stochastic Model
Stochasticity

## Slide 8: Literature Review Review
Previous work
Aaron Olson and Gianluca Geraci (Sandia National Laboratories)
EVADE – Embedded Variance Deconvolution

## Slide 9: Literature Review Review
Previous work
Aaron Olson and Gianluca Geraci (Sandia National Laboratories)
EVADE – Embedded Variance Deconvolution
Current methods
Existing Monte Carlo radiation transport codes (e.g. MCNP, Serpent, KENO)
Adjoint-Based Sensitivity Analysis and Uncertainty Quantification for keff: Using the MCNP KSEN Card[3], (2018)
  MCNP uncertainty analysis for k-eigenvalue problems
Nuclear data uncertainty and sensitivity analysis of the VHTRC benchmark using SCALE[4], (2017)
  Compares random sampling methods with linear perturbation methods
  Discusses influence of particle modeling and nuclear data

## Slide 10: Literature Review Review
Previous work
Aaron Olson and Gianluca Geraci (Sandia National Laboratories)
EVADE – Embedded Variance Deconvolution
“For the comparison of the results using the random sampling approach with SAMPLER [to the results from the continuous linear perturbation models with CE-TSUNAMI], it has to be considered that the results are obtained by a limited sample size. Every output quantity is accompanied by a statistical confidence interval considering the sample size of 1,000.”
Current methods
Existing Monte Carlo radiation transport codes (e.g. MCNP, Serpent, KENO)
Adjoint-Based Sensitivity Analysis and Uncertainty Quantification for keff: Using the MCNP KSEN Card[3], (2018)
  MCNP uncertainty analysis for k-eigenvalue problems
Nuclear data uncertainty and sensitivity analysis of the VHTRC benchmark using SCALE[4], (2017)
  Compares random sampling methods with linear perturbation methods
  Discusses influence of particle modeling and nuclear data

## Slide 11: Background – Sampling uncertainty quantification
Quantity of interest (QoI):
Characterize with
  Mean,
  Variance,
Sampling UQ algorithm:
  Sample UQ parameter
  Solve for QoI with existing solver
  Repeat for UQ samples
  Use sampling-based estimators for statistics
Notes: - an intro to uncertainty quantification
In general, quantity of interest Q, a function of uncertain parameter xi
UQ propagates some source of uncertainty through a numerical code to evaluate statistics
Statistics one might be interested in, using the moment equation. Mean is first moment; variance
You can use a variety of strategies, surrogate and sampling and hybrid
sampling aka MC good for noisy QoI, example alg
In general you have some quantity of interest (or QoI) Q as a result of a numerical code. Uncertainty quantification is the process of propagating some sources of uncertainty through the numerical code to evaluate the statistics of your QoI. Q is then a function of you uncertainty parameter, xi
We have an example here of some statistics of your QoI you might be interested in, as functions of the moment equation. So eq. 1 is the order-p moment equation of Q. Eq 2 is the first moment of Q, aka the expectation or mean. The variance can be taken to be the second moment minus the square of the first moment. A simple example of a stochastic system might look mathematically is eq. 4, where you have some differential equation describing your system, and the parameter xi represents uncertainty in your system.
There are a variety of UQ strategies – surrogates, sampling-based methods, or hybrids of the two. In general, sampling methods (aka MC methods) are good for systems with noisy quantities of interest. Applied to eq. 4, If you have a numerical solver for a solution of y, a sampling UQ approach would be to sample xi and solve for y as a function of it, then do that a number of times (this is referred to as Monte Carlo UQ). Then, calculate your statistics information to understand how your QoI reacts as a function of this uncertain parameter, and we can compare to an exact solution to understand how accurate our sampling approach is.

## Slide 12: Background – Sampling uncertainty quantification
Sampling UQ algorithm:
  Sample UQ parameter
  Solve for QoI with existing solver
  Repeat for UQ samples
  Use sampling-based estimators for statistics
Quantity of interest (QoI):
Characterize with
  Mean,
  Variance,
Notes: - an intro to uncertainty quantification
In general, quantity of interest Q, a function of uncertain parameter xi
UQ propagates some source of uncertainty through a numerical code to evaluate statistics
Statistics one might be interested in, using the moment equation. Mean is first moment; variance
You can use a variety of strategies, surrogate and sampling and hybrid
sampling aka MC good for noisy QoI, example alg
In general you have some quantity of interest (or QoI) Q as a result of a numerical code. Uncertainty quantification is the process of propagating some sources of uncertainty through the numerical code to evaluate the statistics of your QoI. Q is then a function of you uncertainty parameter, xi
We have an example here of some statistics of your QoI you might be interested in, as functions of the moment equation. So eq. 1 is the order-p moment equation of Q. Eq 2 is the first moment of Q, aka the expectation or mean. The variance can be taken to be the second moment minus the square of the first moment. A simple example of a stochastic system might look mathematically is eq. 4, where you have some differential equation describing your system, and the parameter xi represents uncertainty in your system.
There are a variety of UQ strategies – surrogates, sampling-based methods, or hybrids of the two. In general, sampling methods (aka MC methods) are good for systems with noisy quantities of interest. Applied to eq. 4, If you have a numerical solver for a solution of y, a sampling UQ approach would be to sample xi and solve for y as a function of it, then do that a number of times (this is referred to as Monte Carlo UQ). Then, calculate your statistics information to understand how your QoI reacts as a function of this uncertain parameter, and we can compare to an exact solution to understand how accurate our sampling approach is.

## Slide 13: Background – Sampling uncertainty quantification
Sampling UQ algorithm with stochastic solver:
  Sample UQ parameter
  Solve for QoI with existing stochastic solver,
  Repeat for UQ samples
  Use sampling-based estimators for statistics
Quantity of interest (QoI):
Characterize with
  Mean,
  Variance,
Notes: - an intro to uncertainty quantification
In general, quantity of interest Q, a function of uncertain parameter xi
UQ propagates some source of uncertainty through a numerical code to evaluate statistics
Statistics one might be interested in, using the moment equation. Mean is first moment; variance
You can use a variety of strategies, surrogate and sampling and hybrid
sampling aka MC good for noisy QoI, example alg
In general you have some quantity of interest (or QoI) Q as a result of a numerical code. Uncertainty quantification is the process of propagating some sources of uncertainty through the numerical code to evaluate the statistics of your QoI. Q is then a function of you uncertainty parameter, xi
We have an example here of some statistics of your QoI you might be interested in, as functions of the moment equation. So eq. 1 is the order-p moment equation of Q. Eq 2 is the first moment of Q, aka the expectation or mean. The variance can be taken to be the second moment minus the square of the first moment. A simple example of a stochastic system might look mathematically is eq. 4, where you have some differential equation describing your system, and the parameter xi represents uncertainty in your system.
There are a variety of UQ strategies – surrogates, sampling-based methods, or hybrids of the two. In general, sampling methods (aka MC methods) are good for systems with noisy quantities of interest. Applied to eq. 4, If you have a numerical solver for a solution of y, a sampling UQ approach would be to sample xi and solve for y as a function of it, then do that a number of times (this is referred to as Monte Carlo UQ). Then, calculate your statistics information to understand how your QoI reacts as a function of this uncertain parameter, and we can compare to an exact solution to understand how accurate our sampling approach is.

## Slide 14: Background – Sampling uncertainty quantification
Notes: - an intro to uncertainty quantification
In general, quantity of interest Q, a function of uncertain parameter xi
UQ propagates some source of uncertainty through a numerical code to evaluate statistics
Statistics one might be interested in, using the moment equation. Mean is first moment; variance
You can use a variety of strategies, surrogate and sampling and hybrid
sampling aka MC good for noisy QoI, example alg
In general you have some quantity of interest (or QoI) Q as a result of a numerical code. Uncertainty quantification is the process of propagating some sources of uncertainty through the numerical code to evaluate the statistics of your QoI. Q is then a function of you uncertainty parameter, xi
We have an example here of some statistics of your QoI you might be interested in, as functions of the moment equation. So eq. 1 is the order-p moment equation of Q. Eq 2 is the first moment of Q, aka the expectation or mean. The variance can be taken to be the second moment minus the square of the first moment. A simple example of a stochastic system might look mathematically is eq. 4, where you have some differential equation describing your system, and the parameter xi represents uncertainty in your system.
There are a variety of UQ strategies – surrogates, sampling-based methods, or hybrids of the two. In general, sampling methods (aka MC methods) are good for systems with noisy quantities of interest. Applied to eq. 4, If you have a numerical solver for a solution of y, a sampling UQ approach would be to sample xi and solve for y as a function of it, then do that a number of times (this is referred to as Monte Carlo UQ). Then, calculate your statistics information to understand how your QoI reacts as a function of this uncertain parameter, and we can compare to an exact solution to understand how accurate our sampling approach is.

## Slide 15: Methods – Uncertainty quantification
Notes: - an intro to uncertainty quantification
In general, quantity of interest Q, a function of uncertain parameter xi
UQ propagates some source of uncertainty through a numerical code to evaluate statistics
Statistics one might be interested in, using the moment equation. Mean is first moment; variance
You can use a variety of strategies, surrogate and sampling and hybrid
sampling aka MC good for noisy QoI, example alg
In general you have some quantity of interest (or QoI) Q as a result of a numerical code. Uncertainty quantification is the process of propagating some sources of uncertainty through the numerical code to evaluate the statistics of your QoI. Q is then a function of you uncertainty parameter, xi
We have an example here of some statistics of your QoI you might be interested in, as functions of the moment equation. So eq. 1 is the order-p moment equation of Q. Eq 2 is the first moment of Q, aka the expectation or mean. The variance can be taken to be the second moment minus the square of the first moment. A simple example of a stochastic system might look mathematically is eq. 4, where you have some differential equation describing your system, and the parameter xi represents uncertainty in your system.
There are a variety of UQ strategies – surrogates, sampling-based methods, or hybrids of the two. In general, sampling methods (aka MC methods) are good for systems with noisy quantities of interest. Applied to eq. 4, If you have a numerical solver for a solution of y, a sampling UQ approach would be to sample xi and solve for y as a function of it, then do that a number of times (this is referred to as Monte Carlo UQ). Then, calculate your statistics information to understand how your QoI reacts as a function of this uncertain parameter, and we can compare to an exact solution to understand how accurate our sampling approach is.

## Slide 16: Methods – Uncertainty quantification
Goal: from
Notes: - From a UQ standpoint, goal is variance of QoI as a function of uncertain parameter
transmittance T = ratio
*click*
Uncertain param sigT, transmittance as function
*click*
Single code response func of xi
Also rep MC uncertainty mathematically, not a number, vector of RV
*click*
QoI is then expectation over eta,
*click* which must be estimated
Look at statistics, starting with expectation *click*
Expec of T over UQ space, aka first moment from Eq. 2, also approx.
What else do we care about?
So our goal is to obtain the variance of our quantity of interest over a number of UQ samples, and we can start by going through the statistics of our QoI. In this case, our quantity of interest will be transmittance, the ratio of particles that leave the system once they’ve entered. We have our uncertain parameter Sigma_t, and though you wouldn’t say the transport is a ‘function of’ the total cross section, here our quantity of interest transmittance becomes a function of the stochastic total cross section, as in Eq. 6 *click*
If our parameter uncertainty is xi, we can represent the monte carlo solver uncertainty using eta. Eta is not something sampled and plugged in, like xi is, but just mathematically represents the vector of random variables used to follow a particle along its ‘random walk’, and the resulting stochasticity. One UQ sample response would then actually then be the expectation over the entire eta space. We can bring back our first moment equation to find expectation, eq. 2, and this would be exact if we had an infinite number of samples. Instead, we have to settle for an approximation using a finite number ”samples” of our solver’s random behavior for one UQ sample, aka the number N_eta of histories we run per UQ sample. *click*
The first moment of the final code response, aka expectation of T, is also approximated using a finite number of UQ samples N_xi. Plugging Eq. 8 into Eq. 2 gives us Eq. 9, an approximation to the first moment of T using our code responses.

## Slide 17: Methods – Uncertainty quantification
Parameter uncertainty and MCRT uncertainty
Goal: from
Notes: - From a UQ standpoint, goal is variance of QoI as a function of uncertain parameter
transmittance T = ratio
*click*
Uncertain param sigT, transmittance as function
*click*
Single code response func of xi
Also rep MC uncertainty mathematically, not a number, vector of RV
*click*
QoI is then expectation over eta,
*click* which must be estimated
Look at statistics, starting with expectation *click*
Expec of T over UQ space, aka first moment from Eq. 2, also approx.
What else do we care about?
So our goal is to obtain the variance of our quantity of interest over a number of UQ samples, and we can start by going through the statistics of our QoI. In this case, our quantity of interest will be transmittance, the ratio of particles that leave the system once they’ve entered. We have our uncertain parameter Sigma_t, and though you wouldn’t say the transport is a ‘function of’ the total cross section, here our quantity of interest transmittance becomes a function of the stochastic total cross section, as in Eq. 6 *click*
If our parameter uncertainty is xi, we can represent the monte carlo solver uncertainty using eta. Eta is not something sampled and plugged in, like xi is, but just mathematically represents the vector of random variables used to follow a particle along its ‘random walk’, and the resulting stochasticity. One UQ sample response would then actually then be the expectation over the entire eta space. We can bring back our first moment equation to find expectation, eq. 2, and this would be exact if we had an infinite number of samples. Instead, we have to settle for an approximation using a finite number ”samples” of our solver’s random behavior for one UQ sample, aka the number N_eta of histories we run per UQ sample. *click*
The first moment of the final code response, aka expectation of T, is also approximated using a finite number of UQ samples N_xi. Plugging Eq. 8 into Eq. 2 gives us Eq. 9, an approximation to the first moment of T using our code responses.

## Slide 18: Methods – Uncertainty quantification
Parameter uncertainty and MCRT uncertainty
Goal: from
Notes: - From a UQ standpoint, goal is variance of QoI as a function of uncertain parameter
transmittance T = ratio
*click*
Uncertain param sigT, transmittance as function
*click*
Single code response func of xi
Also rep MC uncertainty mathematically, not a number, vector of RV
*click*
QoI is then expectation over eta,
*click* which must be estimated
Look at statistics, starting with expectation *click*
Expec of T over UQ space, aka first moment from Eq. 2, also approx.
What else do we care about?
So our goal is to obtain the variance of our quantity of interest over a number of UQ samples, and we can start by going through the statistics of our QoI. In this case, our quantity of interest will be transmittance, the ratio of particles that leave the system once they’ve entered. We have our uncertain parameter Sigma_t, and though you wouldn’t say the transport is a ‘function of’ the total cross section, here our quantity of interest transmittance becomes a function of the stochastic total cross section, as in Eq. 6 *click*
If our parameter uncertainty is xi, we can represent the monte carlo solver uncertainty using eta. Eta is not something sampled and plugged in, like xi is, but just mathematically represents the vector of random variables used to follow a particle along its ‘random walk’, and the resulting stochasticity. One UQ sample response would then actually then be the expectation over the entire eta space. We can bring back our first moment equation to find expectation, eq. 2, and this would be exact if we had an infinite number of samples. Instead, we have to settle for an approximation using a finite number ”samples” of our solver’s random behavior for one UQ sample, aka the number N_eta of histories we run per UQ sample. *click*
The first moment of the final code response, aka expectation of T, is also approximated using a finite number of UQ samples N_xi. Plugging Eq. 8 into Eq. 2 gives us Eq. 9, an approximation to the first moment of T using our code responses.

## Slide 19: Methods – Uncertainty quantification
Parameter uncertainty and MCRT uncertainty
Goal: from
Law of total variance
Notes: - From a UQ standpoint, goal is variance of QoI as a function of uncertain parameter
transmittance T = ratio
*click*
Uncertain param sigT, transmittance as function
*click*
Single code response func of xi
Also rep MC uncertainty mathematically, not a number, vector of RV
*click*
QoI is then expectation over eta,
*click* which must be estimated
Look at statistics, starting with expectation *click*
Expec of T over UQ space, aka first moment from Eq. 2, also approx.
What else do we care about?
So our goal is to obtain the variance of our quantity of interest over a number of UQ samples, and we can start by going through the statistics of our QoI. In this case, our quantity of interest will be transmittance, the ratio of particles that leave the system once they’ve entered. We have our uncertain parameter Sigma_t, and though you wouldn’t say the transport is a ‘function of’ the total cross section, here our quantity of interest transmittance becomes a function of the stochastic total cross section, as in Eq. 6 *click*
If our parameter uncertainty is xi, we can represent the monte carlo solver uncertainty using eta. Eta is not something sampled and plugged in, like xi is, but just mathematically represents the vector of random variables used to follow a particle along its ‘random walk’, and the resulting stochasticity. One UQ sample response would then actually then be the expectation over the entire eta space. We can bring back our first moment equation to find expectation, eq. 2, and this would be exact if we had an infinite number of samples. Instead, we have to settle for an approximation using a finite number ”samples” of our solver’s random behavior for one UQ sample, aka the number N_eta of histories we run per UQ sample. *click*
The first moment of the final code response, aka expectation of T, is also approximated using a finite number of UQ samples N_xi. Plugging Eq. 8 into Eq. 2 gives us Eq. 9, an approximation to the first moment of T using our code responses.

## Slide 20: Methods – Uncertainty quantification
Parameter uncertainty and MCRT uncertainty
Goal: from
Law of total variance
Notes: - From a UQ standpoint, goal is variance of QoI as a function of uncertain parameter
transmittance T = ratio
*click*
Uncertain param sigT, transmittance as function
*click*
Single code response func of xi
Also rep MC uncertainty mathematically, not a number, vector of RV
*click*
QoI is then expectation over eta,
*click* which must be estimated
Look at statistics, starting with expectation *click*
Expec of T over UQ space, aka first moment from Eq. 2, also approx.
What else do we care about?
So our goal is to obtain the variance of our quantity of interest over a number of UQ samples, and we can start by going through the statistics of our QoI. In this case, our quantity of interest will be transmittance, the ratio of particles that leave the system once they’ve entered. We have our uncertain parameter Sigma_t, and though you wouldn’t say the transport is a ‘function of’ the total cross section, here our quantity of interest transmittance becomes a function of the stochastic total cross section, as in Eq. 6 *click*
If our parameter uncertainty is xi, we can represent the monte carlo solver uncertainty using eta. Eta is not something sampled and plugged in, like xi is, but just mathematically represents the vector of random variables used to follow a particle along its ‘random walk’, and the resulting stochasticity. One UQ sample response would then actually then be the expectation over the entire eta space. We can bring back our first moment equation to find expectation, eq. 2, and this would be exact if we had an infinite number of samples. Instead, we have to settle for an approximation using a finite number ”samples” of our solver’s random behavior for one UQ sample, aka the number N_eta of histories we run per UQ sample. *click*
The first moment of the final code response, aka expectation of T, is also approximated using a finite number of UQ samples N_xi. Plugging Eq. 8 into Eq. 2 gives us Eq. 9, an approximation to the first moment of T using our code responses.

## Slide 21: Methods – Uncertainty quantification
Parametric variance
Average MCRT solver variance
Notes: - an intro to uncertainty quantification
In general, quantity of interest Q, a function of uncertain parameter xi
UQ propagates some source of uncertainty through a numerical code to evaluate statistics
Statistics one might be interested in, using the moment equation. Mean is first moment; variance
You can use a variety of strategies, surrogate and sampling and hybrid
sampling aka MC good for noisy QoI, example alg
In general you have some quantity of interest (or QoI) Q as a result of a numerical code. Uncertainty quantification is the process of propagating some sources of uncertainty through the numerical code to evaluate the statistics of your QoI. Q is then a function of you uncertainty parameter, xi
We have an example here of some statistics of your QoI you might be interested in, as functions of the moment equation. So eq. 1 is the order-p moment equation of Q. Eq 2 is the first moment of Q, aka the expectation or mean. The variance can be taken to be the second moment minus the square of the first moment. A simple example of a stochastic system might look mathematically is eq. 4, where you have some differential equation describing your system, and the parameter xi represents uncertainty in your system.
There are a variety of UQ strategies – surrogates, sampling-based methods, or hybrids of the two. In general, sampling methods (aka MC methods) are good for systems with noisy quantities of interest. Applied to eq. 4, If you have a numerical solver for a solution of y, a sampling UQ approach would be to sample xi and solve for y as a function of it, then do that a number of times (this is referred to as Monte Carlo UQ). Then, calculate your statistics information to understand how your QoI reacts as a function of this uncertain parameter, and we can compare to an exact solution to understand how accurate our sampling approach is.

## Slide 22: Example – Uncertainty quantification
Streaming Particle
1D attenuation problem parameters.
Attenuation through 1D slab, materials
Uncertain total cross sections
Analytic transmittance
Notes: Apply it to a stochastic, one dimensional, neutral-particle, mono-energetic, steady state rad transport problem with a normally incident beam and attenuation-only. The problem has 3 material sections, and table 1 shows the material properties including avg total xsec and variability of the xsec as applied in eq 5
- Saw nested algorithm w/ UQ on outside and RT on inside
So what would that algorithm actually look like for transmittance
Why an attenuation problem and a scattering problem? Reason: attenuation problem to have closed-form solutions and scattering problem to be more realistic and enable looking at two different QoIs to see behavior. You might have said that later, but I don't think you said it here, and it might be helpful.

## Slide 23: Example – Uncertainty quantification
1D radiation transport problem (m=3). 25,000 variance deconvolution repetitions.
Mean QoI and parametric variance.
    , Parametric
    ,
    Total polluted
      Benchmark:
      Variance deconvolution:
Notes: Table on the left shows the results for transmittance and parametric variance for a benchmark (overresolved) configuration, just one repetition (which is a sample), and the analytic results.
Repeated algorithm 25,000 times to get statistics of estimate of varT and varTtilde
300 Nxi 5 Neta
Clustered around analytic solution, estimators are unbiased
Strong indication that we get a good estimate of our variances
For a sample problem with 300 UQ samples and 5 particles per sample with 25,000 repetitions. Clustered around analytic solution, bc estimators are unbiased.

## Slide 24: Methods – UQ cost analysis
as a function of for a variety of total estimator costs, log-log plot. Unfilled point is minimum .
Total estimator cost
Notes: Repeated algorithm 25,000 times to get statistics of estimate of varT and varTtilde
300 Nxi 5 Neta
Clustered around analytic solution, estimators are unbiased
Strong indication that we get a good estimate of our variances
Poster compares to previously developed method
Other work includes varying Nxi and Neta, adding in scattering problem
For a sample problem with 300 UQ samples and 5 particles per sample with 25,000 repetitions. Clustered around analytic solution, bc estimators are unbiased. Poster does comparison w/ other method

## Slide 25: Methods – UQ cost analysis
as a function of for a variety of total estimator costs, log-log plot. Unfilled point is minimum .
Total estimator cost
Notes: Repeated algorithm 25,000 times to get statistics of estimate of varT and varTtilde
300 Nxi 5 Neta
Clustered around analytic solution, estimators are unbiased
Strong indication that we get a good estimate of our variances
Poster compares to previously developed method
Other work includes varying Nxi and Neta, adding in scattering problem
For a sample problem with 300 UQ samples and 5 particles per sample with 25,000 repetitions. Clustered around analytic solution, bc estimators are unbiased. Poster does comparison w/ other method

## Slide 26: Methods – UQ cost analysis
For given cost, find such that
Variance of a sample estimator:
Independent variable
Sample estimator:

## Slide 27: Methods – UQ cost analysis
Analytically calculate all terms in equation
scipy.optimize.brentq() finds 0 of function on a given interval using Brent’s method
Analytically calculate all terms in equation
Goal: pilot study to numerically calculate needed terms
as a function of for a variety of total estimator costs, log-log plot.
Notes: Estimator is unbiased, ie we converge to the mean with no biasing error introduced
For a given total estimator cost, like 2000 total histories, there’s various combinations of Nxi and Neta possible
Goal: minimized variance of S^2, aka deviation from mean

## Slide 28: Background – Global sensitivity analysis
Variance-based sensitivity analysis
Multiple uncertainty sources in model
Main effect ( indicates all variables except )
Interaction effect
Provides global response

## Slide 29: Background – Global sensitivity analysis
Sensitivity indices (Sobol indices)
First order sensitivity index
Total order/effect index main effect and all interactions
Variance-based sensitivity analysis
Multiple uncertainty sources in model
Main effect ( indicates all variables except )
Interaction effect
Provides global response

## Slide 30: Background – Global sensitivity analysis
Sensitivity indices (Sobol indices)
First order sensitivity index
Total order/effect index main effect and all interactions
Variance-based sensitivity analysis, stochastic solver
Multiple uncertainty sources in model
Main effect ( indicates all variables except )
Interaction effect
Provides global response

## Slide 31: Example – Global sensitivity analysis
Streaming Particle
Attenuation through 1D slab, materials
Uncertain total cross section
Stochastic media region with sub-cells of with probability or
  Number of sub-cells with :
Notes: Apply it to a stochastic, one dimensional, neutral-particle, mono-energetic, steady state rad transport problem with a normally incident beam and attenuation-only. The problem has 3 material sections, and table 1 shows the material properties including avg total xsec and variability of the xsec as applied in eq 5
- Saw nested algorithm w/ UQ on outside and RT on inside
So what would that algorithm actually look like for transmittance
Why an attenuation problem and a scattering problem? Reason: attenuation problem to have closed-form solutions and scattering problem to be more realistic and enable looking at two different QoIs to see behavior. You might have said that later, but I don't think you said it here, and it might be helpful.

## Slide 32: Example – Global sensitivity analysis
Streaming Particle
Attenuation through 1D slab, materials
Uncertain total cross section
Notes: Apply it to a stochastic, one dimensional, neutral-particle, mono-energetic, steady state rad transport problem with a normally incident beam and attenuation-only. The problem has 3 material sections, and table 1 shows the material properties including avg total xsec and variability of the xsec as applied in eq 5
- Saw nested algorithm w/ UQ on outside and RT on inside
So what would that algorithm actually look like for transmittance
Why an attenuation problem and a scattering problem? Reason: attenuation problem to have closed-form solutions and scattering problem to be more realistic and enable looking at two different QoIs to see behavior. You might have said that later, but I don't think you said it here, and it might be helpful.

## Slide 33: Example – Global sensitivity analysis
Streaming Particle
Attenuation through 1D slab, materials
Uncertain total cross section
Notes: Apply it to a stochastic, one dimensional, neutral-particle, mono-energetic, steady state rad transport problem with a normally incident beam and attenuation-only. The problem has 3 material sections, and table 1 shows the material properties including avg total xsec and variability of the xsec as applied in eq 5
- Saw nested algorithm w/ UQ on outside and RT on inside
So what would that algorithm actually look like for transmittance
Why an attenuation problem and a scattering problem? Reason: attenuation problem to have closed-form solutions and scattering problem to be more realistic and enable looking at two different QoIs to see behavior. You might have said that later, but I don't think you said it here, and it might be helpful.

## Slide 34: Example – Global sensitivity analysis
Streaming Particle
Attenuation through 1D slab, materials
Uncertain total cross section
Notes: Apply it to a stochastic, one dimensional, neutral-particle, mono-energetic, steady state rad transport problem with a normally incident beam and attenuation-only. The problem has 3 material sections, and table 1 shows the material properties including avg total xsec and variability of the xsec as applied in eq 5
- Saw nested algorithm w/ UQ on outside and RT on inside
So what would that algorithm actually look like for transmittance
Why an attenuation problem and a scattering problem? Reason: attenuation problem to have closed-form solutions and scattering problem to be more realistic and enable looking at two different QoIs to see behavior. You might have said that later, but I don't think you said it here, and it might be helpful.

## Slide 35: Example – Global sensitivity analysis
Streaming Particle
Attenuation through 1D slab, materials
Uncertain total cross section
Notes: Apply it to a stochastic, one dimensional, neutral-particle, mono-energetic, steady state rad transport problem with a normally incident beam and attenuation-only. The problem has 3 material sections, and table 1 shows the material properties including avg total xsec and variability of the xsec as applied in eq 5
- Saw nested algorithm w/ UQ on outside and RT on inside
So what would that algorithm actually look like for transmittance
Why an attenuation problem and a scattering problem? Reason: attenuation problem to have closed-form solutions and scattering problem to be more realistic and enable looking at two different QoIs to see behavior. You might have said that later, but I don't think you said it here, and it might be helpful.

## Slide 36: Example – Global sensitivity analysis
First- and total- order sensitivity indices for and using variance deconvolution.
Transmittance through slab as function of cross-section uncertainty , material mixing uncertainty , and MCRT uncertainty .
Notes: Apply it to a stochastic, one dimensional, neutral-particle, mono-energetic, steady state rad transport problem with a normally incident beam and attenuation-only. The problem has 3 material sections, and table 1 shows the material properties including avg total xsec and variability of the xsec as applied in eq 5
- Saw nested algorithm w/ UQ on outside and RT on inside
So what would that algorithm actually look like for transmittance
Why an attenuation problem and a scattering problem? Reason: attenuation problem to have closed-form solutions and scattering problem to be more realistic and enable looking at two different QoIs to see behavior. You might have said that later, but I don't think you said it here, and it might be helpful.

## Slide 37: Background – Global sensitivity analysis
Saltelli Method for d inputs
Generate 2 matrices and
Construction of Saltelli matrices[5] with , .

## Slide 38: Background – Global sensitivity analysis
Saltelli Method for d inputs
Generate 2 matrices and
Build more matrices for such that except the column, which is the column of
Construction of Saltelli matrices[5] with , .

## Slide 39: Background – Global sensitivity analysis
Saltelli Method for d inputs
Generate 2 matrices and
Build more matrices for such that except the column, which is the column of
Compute using
Construction of Saltelli matrices[5] with , .

## Slide 40: Background – Global sensitivity analysis
Saltelli Method for d inputs
Generate 2 matrices and
Build more matrices for such that except the column, which is the column of
Compute using
Construction of Saltelli matrices[5] with , .
MCRT

## Slide 41: Methods – Challenge problem
Total UQ estimator cost assumes linear cost model

## Slide 42: Methods – Challenge problem
Total UQ estimator cost assumes linear cost model
Reality: runtimes vary
Stochastic media GSA example estimator cost

## Slide 43: Methods – Challenge problem
Subset of Center for Exascale Monte Carlo Neutron Transport (CEMeNT) challenge problem
NuScale-like small modular reactor (SMR), cross-section at left[6]

## Slide 44: Methods – Challenge problem
Our challenge problem: Phase 1
Time-dependent version of fixed source problem with active neutron source
Spatial asymmetry due to stuck rods
CEMeNT challenge problem[6].
Total fission rate results from MC/DC with histories[6,7].

## Slide 45: Progress – Uncertainty quantification
Accurate and efficient UQ with stochastic computational solvers
Develop theoretical framework for forward uncertainty propagation which accounts for the additional variability introduced by the stochastic solver.
Complete
Complete
Complete
Publications
0.*. K. Clements, G. Geraci, and A. Olson, “A Variance Deconvolution Approach to Sampling Uncertainty Quantification for Monte Carlo Radiation Transport Solvers,” in “Computer Science Research Institute Summer Proceedings 2021,” (2021), Technical Report SAND2022-0653R, pp.293-307.
K. Clements, G. Geraci, A. Olson, “Numerical Investigation on the Performance of a Variance Deconvolution Estimator,” in ”Transactions of the American Nuclear Society,” (Jun 2022).
[In progress] K. Clements, G. Geraci, A. Olson, T. Palmer, “A Variance Deconvolution Estimator for Efficient Uncertainty Quantification in Monte Carlo Radiation Transport Problems,” (2023)
Validate estimator with attenuation through a 1D slab.
Develop an optimization method to determine an ideal ratio of MCUQ samples to MCRT histories for a set cost constraint.
K. Clements, G. Geraci, and A. Olson, “A Variance Deconvolution Approach to Sampling Uncertainty Quantification for Monte Carlo Radiation Transport Solvers,” in “Computer Science Research Institute Summer Proceedings 2021,” (Aug 2021), Technical Report SAND2022-0653R, pp.293-307.

## Slide 46: Progress – Global sensitivity analysis
Accurate and efficient GSA with stochastic computational solvers
Explore existing methods for stochastic solvers in GSA.
Ongoing
Ongoing
Publications
A. Olson, K. Clements, J. Petticrew, “A sampling-based approach to solve Sobol’ Indices using variance deconvolution for arbitrary uncertainty distributions,” in “Transactions of the American Nuclear Society,” (Nov 2022).
[Accepted with minor revisions] K. Clements, G. Geraci, A. Olson, T. Palmer, “Global Sensitivity Analysis in Monte Carlo Radiation Transport,” in “Transactions of the International Conference on Mathematics and Computational Methods Applied to Nuclear Science and Engineering,” (Aug 2023).
Use surrogate approach with deterministic and stochastic solvers to understand what variability is introduced.
Use Saltelli approach with deterministic and stochastic solvers to understand what variability is introduced.
Apply variance deconvolution to sensitivity indices.

## Slide 47: Progress – Challenge problem
Apply developed methods to complex radiation transport problem
Integrate variance deconvolution for UQ into MC/DC.
Ongoing
Test MC/DC GSA integration with complex radiation transport problem.
Develop complex cost model tunable for efficient MCUQ/MCRT sampling.
Fully integrate methods into MC/DC for sensitivity studies.

## Slide 48: Proposed schedule

## Slide 49: Questions

## Slide 50: Citations
Connection between Observation, Model, and Simulation. (2018). In Wikipedia. Retrieved January 31, 2023 from https://wiki.its.sfu.ca/permanent/learning/index.php/File:CompModelFig1.png#file.
Lopez, Rafael & Beck, André. (2013). Advanced Structured Materials. doi:10.1007/978-3-319-00717-5_8.
Favorite, Jeffrey A. Adjoint-Based Sensitivity Analysis and Uncertainty Quantification for keff: Using the MCNP KSEN Card. (2018). Los Alamos National Laboratory. doi:10.2172/1467190.
Bostelmann, Friederike & Strydom, Gerhard. (2017). Nuclear data uncertainty and sensitivity analysis of the VHTRC benchmark using SCALE. Idaho National Laboratory. doi:10.1016/j.anucene.2017.06.052.
Becker, Will. Construction of ABi matrices in monte carlo estimation of sensitivity indices. (2012). In Wikipedia. Retrieved January 31, 2023 from https://commons.wikimedia.org/w/index.php?curid=22396140.
McClarren, Ryan. SMR Challenge Problem: Definition and progress on our demonstration problem. CEMeNT presentation to PSAAP review team. (2022).
Variansyah, Ilahm. MC/DC: Monte Carlo Dynamic Code. (2022-ongoing). https://github.com/CEMeNT-PSAAP/MCDC.